## Slide 1: ECE 353 Introduction to Microprocessor Systems
Circular Buffers
Notes: This video will cover the principles of circular buffers.

## Slide 2: Software Circular Buffer
Allows the application to write data into part of SRAM and continue on
Accessing a circular buffer is very fast. It is simply an array of memory
The SRAM overhead for managing is very small. Depending on implementation, software needs only the address of the array, an index, and a count
Fixed size
Utilizes the modulus operation
Notes: A circular is a very common and widely used data structure in embedded software design. The purpose of a circular buffer is to provide a way store data into a temporary location in SRAM.
A circular buffer has several characteristics that make it a good fit for temporary data storage. The first characteristic of a circular buffer is that adding and removing data is very fast. A circular buffer is really nothing more than an array. Depending on the implementation, a circular buffer will also have a way of determining the index for inserting data and the index for removing data. When software wishes to add data to a circular buffer, it can do so by simply storing the data to the next free location in the array and then updating the index. Loading and storing data using a base address and an index is a very fast operation.
The second characteristic of a circular buffer is that we will look at is the memory footprint required to support the circular buffer. A circular buffer has very little memory overhead to actually manage the circular buffer. The only storage needed in addition to the array itself are the two memory locations used to indicate where data is read from and where data is written to. We can compare this with a linked list. For a basic linked list of characters, each character stored in the linked list would require 5 bytes of data. One byte for the data and four bytes for the pointer to the next character. If I’m trying to store 80 characters, a linked list would consume 400 bytes. Using a circular buffer, I need 80 bytes for the 80 characters plus another 8 bytes to store the producer and consumer counts. In a memory constrained system like a microcontroller, low memory overhead is very important.
Unlike a linked list, a circular buffer is of a fixed size. In order for us to use a circular buffer effectively, we need to make sure that data is being removed from the circular buffer at a reasonable rate to ensure that the circular buffer does not fill up. If the circular buffer fills up, the application will either have to wait for some other task to consume data from the circular buffer or the application can choose to overwrite data in the buffer. Overwriting data is never a good option because our system is essentially loosing data.

## Slide 3: Circular Buffers
buffer_add(0);
buffer_add(1);
buffer_add(2);
buffer_remove(&data);
buffer_add(3);
buffer_add(4);
buffer_add(5);
buffer_add(6);
buffer_add(7);
buffer_add(8);
P
C
0
1
2
3
4
5
6
7
8
Notes: Let’s take a look at how the basic principle of a circular buffer works. The circular buffer we will use in class will use two counts: A produce count and a consume count.
When data is added to the circular buffer, the produce count is incremented. When data is removed from the circular buffer, the consume count is incremented. These two counts will only be incremented. Using these two counts and the modulus operator, we can insert and remove data from the circular buffer.
CLICK
When I add a byte of data to the circular buffer, the data is written to the entry in the circular buffer indicated by the produce count. After the data is written, the produce count is updated.
CLICK
Each time that I add data to the circular buffer, the data is written to the next free entry in the buffer and then the produce count is updated.
CLICK
CLICK
When data is removed from the circular buffer, the consume count is incremented.
CLICK
CLICK CLICK CLICK
Data can be inserted into the circular buffer until the circular buffer is full. We can determine if the circular buffer is full by subtracting the consume count from the produce count. If this value is equal to the size of the array, then the buffer is full and we cannot add any more data to the circular buffer.

## Slide 4: Modulus Arithmetic
buffer_add(5);
buffer_add(6);
buffer_add(7);
buffer_add(8);
buffer_add(9);
P
C
20000000 + (5%8) = 0x20000005
20000000 + (6%8) = 0x20000006
20000000 + (7%8) = 0x20000007
20000000 + (8%8) = 0x20000000
20000000 + (9%8) = 0x20000001
20000000 + (10%8) = 0x20000002
PRODUCE COUNT
5
PRODUCE COUNT
6
PRODUCE COUNT
7
PRODUCE COUNT
8
PRODUCE COUNT
9
PRODUCE COUNT
10
CONSUME COUNT
4
Number of Entries =
PRODUCE COUNT – CONSUME COUNT
Notes: This example should give some insight into how the modulus operator and the produce and consume counts are used to determine where to insert the next value in the circular buffer.
We are going to assume that the consume count is currently equal to four and the produce count is equal to five.
When we want to add the next value into the circular buffer, we need to take the produce count and apply the modulus operator. In this case, 5 modulus with 8 results in a value of 5. We then take that value and add it to the base address of the array.
CLICK
Once the base address is calculated, we can store the value into the buffer.
CLICK
We then increment the produce count.
CLICK
This will happen for each entry into the circular buffer.
CLICK
CLICK
CLICK
CLICK
CLICK
CLICK
CLICK
Now that the produce count is equal to 8, we can see how the modulus operator give us the circular nature of a circular buffer.
CLICK
When we take 8 and apply the modulus operation with a size of 8, the result is 0. When we add zero the to base address, we can see how the insertion wraps around the beginning of the array
CLICK
CLICK
CLICK
CLICK
Here we see that 9 Modulus 8 results in an offset of 1, so the new data is added to address 0x20000001.
CLICK
CLICK
CLICK
In order to determine how many data entries are currently in the circular buffer, we need to use both the produce and consume counts.
CLICK
By subtracting the consume count from the produce count, we can determine the number of entries. In this case, 10 – 4 is equal to 6, which matches what we see in the array.